## Slide 1: gr-plasma A New GNU Radio-based Tool for Software-defined Radar
Shane Flandermeyer1,2
Rylee Mattingly1,2
Dr. Justin Metcalf1,2
1Advanced Radar Research Center, University of Oklahoma, Norman, Oklahoma, USA
2School of Electrical and Computer Engineering, University of Oklahoma, Norman, OK, USA

## Slide 2: Outline
Introduction
gr-plasma blocks and features overview
  Waveform generators
  USRP interfacing and Control
  Signal processing blocks
  Miscellaneous blocks
Experimental Demonstration
Conclusions and Future Work

## Slide 3: Introduction
Experimental radar systems traditionally lacked flexibility
  Required expensive custom hardware for real time operation
Developments in SDR hardware and GPUs make RF research more accessible
  Real time operation possible with COTS components
  High-level tools like CUDA and GNU Radio significantly reduce development time
Most SDR tools designed for communications, not radar

## Slide 4: Introduction
Challenges in software-defined radar operation
  Transmit and receive processes must be synchronized to the sample level for localization accuracy
  Reliable high-speed duplex operation required for waveforms with large bandwidths
  Processing intervals too large for GNU Radio stream buffers

## Slide 5: Introduction
Primarily considering pulsed radar operation
  Radar pulses processed as bursty packets
  A natural fit for the message passing interface!

## Slide 6: The gr-plasma [1] module
An end-to-end radar processing toolbox in the message passing domain
Current capabilities include:
  Waveform generation (pulsed and CW)
  USRP control and calibration
  Pulse-doppler processing
Processing implemented in separate plasma_dsp [2] repository
  Easy to drop in other C++ or Python projects

## Slide 7: USRP Interfacing and Control

## Slide 8: USRP Radar Module
Combines USRP source and sink into a single block
Minimizes data transfer by repeatedly transmitting last PDU received
  Internally handles timing to avoid under/overflows at higher sample rates
Outputs each pulse as timed PDU

## Slide 9: USRP Delay Calibration
Problem: Internal USRP DSP produces a constant delay
  Produces offset from true range in radar processing
  Constant value for a given radio's sample rate/master clock rate

## Slide 10: USRP Delay Calibration
Problem: Internal USRP DSP produces a constant delay
  Produces offset from true range in radar processing
  Constant value for a given radio's sample rate/master clock rate
Solution: Use a script to automate calibration
  Inspired by Estimator Sync Pulse block in gr-radar

## Slide 11: Waveform Generators

## Slide 12: Linear FM (LFM) Waveforms
Most common radar waveform
  Sweeps linearly across its bandwidth B over time interval Tp
  LFM source block centers sweep around DC

## Slide 13: Polyphase-Coded FM (PCFM) Waveforms
Newer waveform class (first introduced in [3])
Inspired by continuous phase modulation (CPM)
  Modulates a phase code instead of communications symbols
More degrees of freedom for waveform optimization

## Slide 14: Signal Processing Blocks

## Slide 15: GPU Integration
ArrayFire used to greatly simplify GPU computation
  Has optimized functions for common signal processing operations
  CPU, CUDA, and OpenCL backends
  Multi-GPU support
Backend is a block parameter
  All blocks in flowgraph must use the same in gr-plasma v1.0

## Slide 16: Matched Filtering
Cross-correlation between transmitted and received signals
Used to detect signals in high-power noise
Delay of peak depends on range of scatterer
Width of peak depends on waveform bandwidth

## Slide 17: Doppler Processing
Step 1: Collect N matched filter responses of length L into the columns of a matrix
  N = Number of pulses in a coherent processing interval (CPI)
Step 2: Compute an FFT across each row
  Transforms pulse dimension to doppler frequency
  Resulting matrix is a range-doppler map

## Slide 18: Pulse-Doppler Processing
Matched filtering and doppler processing usually performed sequentially
Can use separate blocks, but wastes memory and computation
  Need two identical copies of some variables
  Must copy data to/from PDU messages
The Pulse-Doppler Processing block solves these problems

## Slide 19: Additional Blocks
PDU File Source/Sink: Convert data and metadata to PDU and vice versa
  Data loading is identical to in-tree File Source/Sink
  Metadata saved as JSON and loaded as PMT dictionary
  SigMF compatible!

## Slide 20: Additional Blocks
Pulse to CPI: Combine N smaller PDUs into a single large PDU
PDU Head: Copy the first N PDUs to the output and consume the rest
Waveform Controller: Add a pulse repetition frequency (PRF) entry to waveform metadata dictionary
  Puts USRP Radar in burst mode
  Plan to eventually implement more complex logic (e.g., resource management)

## Slide 21: Experimental Setup
USRP B210 in monostatic configuration
Vehicles moving radially to/from the radar

## Slide 22: Results
Clearly visible returns in 300 m scene
Multiple targets visible
Animation captured directly from GNU Radio

## Slide 23: Conclusions
gr-plasma is an OOT module for collecting and processing radar data
  Uses GNU Radio's message passing architecture
  heterogeneous processing with CPU, CUDA, and OpenCL
Currently has blocks for
  Radar waveform generation
  Pulse-doppler processing
  Range-Doppler map visualizations
Demonstrated with an open-air real time experiment

## Slide 24: Future Work
Develop more signal processing blocks
  Constant False Alarm Rate (CFAR) detector implemented in develop branch
Close the cognitive loop
  Modify waveform in USRP Radar based on downstream processing
  Waveform controller block intended to handle this logic

## Slide 25: References
[1] https://github.com/ShaneFlandermeyer/gr-plasma
[2] https://github.com/ShaneFlandermeyer/plasma-dsp.git
[3] S. D. Blunt, M. Cook, J. Jakabosky, J. De Graaf and E. Perrins, "Polyphase-coded FM (PCFM) radar waveforms, part I: implementation," in IEEE Transactions on Aerospace and Electronic Systems, vol. 50, no. 3, pp. 2218-2229, July 2014, doi: 10.1109/TAES.2014.130361.

## Slide 26
Advanced Radar Research Center
http://arrc.ou.edu