## Slide 1: High Accuracy Wireless Timing Synchronization Using Software Defined Radios
Jason M. Merlo and Jeffrey A. Nanzer
2023 GNU Radio Conference
High Performance SDR Applications

## Slide 2
Motivation and Applications
Synchronization Technique
Software Overview & Demo
Experimental Results

## Slide 3: 1 | Motivation and Applications

## Slide 4: Motivation // Coherent Distributed Antenna Arrays
Far-Field Information Wavefront
Far-Field Information Wavefront
Traditional Phased Array
Distributed Phased Array
Time Synchronization
Frequency Synchronization

## Slide 5: Applications of Coherent Distributed Arrays
Single-platform
resolution
Distributed array
resolution
Precision Agricultural Sensing
Distributed V2X Sensing
Space Communication
and Remote Sensing
Next Generation Satellite Cellular Networks
Receiver or
imaging target
Earth-Based
communication
base station
Sensing and
communication
relay satellite
constellation

## Slide 6: Coherent Distributed Array Synchronization
Time Synchronization
Phase Alignment
Frequency Syntonization
Node: 1
Node: 2
Wireless
Coordination
1
1

## Slide 7: 2 | Synchronization Technique

## Slide 8: System Time Model
Local time at node :
  : true time
  : time-varying offset from global true time
  : other zero-mean noise sources
Goal:
  Estimate and compensate for
Node: 0
Node:
Relative Clock Alignment

## Slide 9: Time Synchronization Overview
Two-Way Time Synchronization
Assumptions:
  Link is reciprocal quasi-static during the synchronization epoch
Timing skew estimate:
Inter-node range estimate:
For compactness of notation:

## Slide 10: High Accuracy Delay Estimation
[3] J. A. Nanzer and M. D. Sharp, “On the Estimation of Angle Rate in Radar,” IEEE T Antenn Propag, vol. 65, no. 3, pp. 1339–1348, 2017, doi: 10.1109/tap.2016.2645785.
The delay accuracy lower bound (CRLB) for time is given by
  : mean-squared bandwidth
  : noise power spectral density
  : signal energy
  : post-processed SNR
Fractional Occupied Bandwidth ()
Relative Mean Sq. Bandwidth

## Slide 11: High Accuracy Delay Estimation
[3] J. A. Nanzer and M. D. Sharp, “On the Estimation of Angle Rate in Radar,” IEEE T Antenn Propag, vol. 65, no. 3, pp. 1339–1348, 2017, doi: 10.1109/tap.2016.2645785.
Fractional Occupied Bandwidth ()
Relative Mean Sq. Bandwidth
For constant-SNR, maximizing will yield improved delay estimation

## Slide 12: Delay Estimation
Discrete matched filter (MF) used in initial time delay estimate
High SNR typically required to disambiguate correct peak
Many other waveforms exist which balance accuracy and ambiguity
[4] J. M. Merlo, S. R. Mghabghab and J. A. Nanzer, "Wireless Picosecond Time Synchronization for Distributed Antenna Arrays," in IEEE Transactions on Microwave Theory and Techniques, vol. 71, no. 4, pp. 1720-1731, April 2023, doi: 10.1109/TMTT.2022.3227878.

## Slide 13: Delay Estimation Refinement
MF causes estimator bias due to time discretization limited by sample rate
Refinement of MF obtained using Quadratic Least Squares (QLS) fitting to find true delay based on three sample points
where
[4] J. M. Merlo, S. R. Mghabghab and J. A. Nanzer, "Wireless Picosecond Time Synchronization for Distributed Antenna Arrays," in IEEE Transactions on Microwave Theory and Techniques, vol. 71, no. 4, pp. 1720-1731, April 2023, doi: 10.1109/TMTT.2022.3227878.

## Slide 14: Delay Estimation Refinement
QLS results in small residual bias due to an imperfect representation of the underlying MF output
Residual bias is a function of waveform and sample rate
Can be easily corrected via lookup table
[4] J. M. Merlo, S. R. Mghabghab and J. A. Nanzer, "Wireless Picosecond Time Synchronization for Distributed Antenna Arrays," in IEEE Transactions on Microwave Theory and Techniques, vol. 71, no. 4, pp. 1720-1731, April 2023, doi: 10.1109/TMTT.2022.3227878.

## Slide 15: 3 | Software Overview

## Slide 16: Software Challenges
High/full sample rate with low CPU utilization
  Use “bursty” transmission scheme
Reasonably low latency
  Use message/PDU-based flowgraph
Maintain groupings of PDUs for each channel transmitted/received
  Use lists of PDUs; initially created a “Wide PDU” type, but switched for compatibility with existing codebase

## Slide 17: Software Guiding Principles
Code reusability
  Implemented on top of DELTA Python Package for code reusability
Implementation/iteration speed
  Scientific processing implemented in Python first, data manipulation in C++
  Benchmark, re-implement in C++ if necessary

## Slide 18: Time Estimation Process
4
3
N0
N1
t
t
RX Window
TX Window
Matched
Filter
Peak-Find
QLS Estimate
Matched
Filter
Peak-Find
QLS Estimate
1
2
4
3
Processing
2
4
are shared between nodes to determine corrections
2
1
TX Window
RX Window
Processing
Generate Waveform
Generate Waveform

## Slide 19: Time Transfer Flow Graph

## Slide 20: Wavegen Block

## Slide 21: USRP Sync Burst Block

## Slide 22: PDU Matched Filter Block

## Slide 23: PDU QLS Peak Estimator Block

## Slide 24: Time Sync Controller Block

## Slide 25: Software Demo

## Slide 26: Software Demo
Time Transfer Antennas
Radios (X310s)
Coordination Server

## Slide 28: 4 | Experimental Results Beamforming

## Slide 29: System Configuration
2–5 m
Manually muted ~100s of milliseconds
[5] J. M. Merlo, A. Schlegel and J. A. Nanzer, "High Accuracy Wireless Time-Frequency Transfer For Distributed Phased Array Beamforming," in 2023 IEEE/MTT-S International Microwave Symposium - IMS 2023, San Diego, CA, USA, 2023.

## Slide 30: System State Flow
Initial PPS Sync
TWTT Exchange
 Update
Transmit beamforming pulses
Estimate and at target
Coarse alignment ~10 ns
Residual bias compensated to picosecond level
Compensate using , and beamsteer using and
First Pulse?
No
Save and as calibration
Yes
Start
Beamsteering
[5] J. M. Merlo, A. Schlegel and J. A. Nanzer, "High Accuracy Wireless Time-Frequency Transfer For Distributed Phased Array Beamforming," in 2023 IEEE/MTT-S International Microwave Symposium - IMS 2023, San Diego, CA, USA, 2023.

## Slide 31: Performance Evaluation Waveforms
Each node transmitted orthogonal LFMs followed by two CW pulses
…
…
Node 1
Node 0
t
t
LFM: Time/Phase Estimation
CW Pulses: Coherent Gain Estimation
[5] J. M. Merlo, A. Schlegel and J. A. Nanzer, "High Accuracy Wireless Time-Frequency Transfer For Distributed Phased Array Beamforming," in 2023 IEEE/MTT-S International Microwave Symposium - IMS 2023, San Diego, CA, USA, 2023.

## Slide 32: Experimental Configuration
Transmit Nodes Setup
Target Node Setup (41 m downrange)
2.1 m
[5] J. M. Merlo, A. Schlegel and J. A. Nanzer, "High Accuracy Wireless Time-Frequency Transfer For Distributed Phased Array Beamforming," in 2023 IEEE/MTT-S International Microwave Symposium - IMS 2023, San Diego, CA, USA, 2023.

## Slide 33: Beamforming Results
Induced Frequency Transfer Failure
[5] J. M. Merlo, A. Schlegel and J. A. Nanzer, "High Accuracy Wireless Time-Frequency Transfer For Distributed Phased Array Beamforming," in 2023 IEEE/MTT-S International Microwave Symposium - IMS 2023, San Diego, CA, USA, 2023.
Notes: Time Transfer SNR: ~23dB
Cycle Time: ~4 s
Beamforming Std.: ps
Phase Std.:
Throughput (BPSK): Gbps
Max Carrier Freq.: GHz
Time Transfer SNR: ~23dB
Cycle Time: ~4 s
Beamforming Std.: 18<𝜎_bf<40 ps
Phase Std.: 0.04𝜋<𝜎_𝜙<0.10𝜋
Throughput (BPSK): 2.5<𝑏_max<5.5 Gbps
Max Carrier Freq.: 1.0<𝑓_max<2.78 GHz

## Slide 34: Beamforming Results
[5] J. M. Merlo, A. Schlegel and J. A. Nanzer, "High Accuracy Wireless Time-Frequency Transfer For Distributed Phased Array Beamforming," in 2023 IEEE/MTT-S International Microwave Symposium - IMS 2023, San Diego, CA, USA, 2023.
mV
mV
mV
V

## Slide 35: Measurement Summary
Demonstrated fully wireless outdoor time-frequency synchronization and beamforming with over a 41 m
Internode Distance | Min. Time Transfer Std. | Min. Beamforming Std. | Max. Throughput* | Max. Carrier Frequency†
2.1 m | 10.47 ps | 18.00 ps | 5.56 Gbps | 2.78 GHz
5.0 m | 14.79 ps | 24.02 ps | 4.16 Gbps | 2.08 GHz
* Maximum theoretical BPSK throughput;
† Maximum theoretical carrier frequency;
[5] J. M. Merlo, A. Schlegel and J. A. Nanzer, "High Accuracy Wireless Time-Frequency Transfer For Distributed Phased Array Beamforming," in 2023 IEEE/MTT-S International Microwave Symposium - IMS 2023, San Diego, CA, USA, 2023.

## Slide 36: Project Status and Conclusion
In Progress:
Standardizing inter-block communications (use PDUs/list of PDUs)
Complete fully distributed compute software implementation
  Testing in progress
Adding/improving documentation
Planned Work:
Add test cases for CI/CD
Open source releases
Investigate use of streaming interface with managed latency to leverage existing streaming blocks

## Slide 37: Questions?
National
Science
Foundation
Thank you to our project sponsors and collaborators:
This work was supported under the auspices of the U.S. Department of Energy by Lawrence Livermore National Laboratory under Contract DEAC52-07NA27344, by the LLNL-LDRD Program under Project No. 22-ER-035, by the Office of Naval Research under grant #N00014-20-1-2389, and by the National Science Foundation under Grant #1751655.
merlojas@msu.edu