## Slide 1
5G Base-Station with Hardware Acceleration for Non-Terrestrial Networks on a Space-Grade System-on-Chip
Michael Petry 1,2, Michael Hennerich 3, Raphael Mayr 1
PhD Student
Michael.petry@airbus.com
Gnu Radio Conference 2024, 18th of September, 2024
FPGA Engineer
Raphael.mayr@airbus.com
1
2
3
Sr. Director, ADI Fellow
michael.hennerich@analog.com

## Slide 2
Existing Mobile Satellite Solutions
Service: Emergency Message
Send & Receive
Partner: Globalstar
Satellites: 24 + 1 (spare)
Type: Transparent
ISL: No
85% network capacity reserved for Apple
Coverage: non polar
No ISL: Gateway must be in sight
Linkbudget / Speed: ?
Satellite Technology / Beams
2
GRCon 18th Sept. 2024, 5G NTN Presentation, M. Petry

## Slide 3
iPhone SOS – A proprietary solution
C-Band
6875 – 7055 MHz
C-Band
5091 –5250 MHz
Uplink
L-Band: 1610 – 1618.7 MHz
Bandwidth: 200 kHz 1
Power: 26 dBm 1
Chip: Custom (?)
Waveform: SC-OFDMA (LTE-UL)
Downlink
S-Band: 2483.5 – 2500 MHz
Chip: Snapdragon X65 / X70
Waveform: CDMA
1 14040866-E22V1 FCC_IC MSS Report
Transparent Satellite (Bent-Pipe)
Frequency Conversion
No On-Board Processing
No Storage
3
GRCon 18th Sept. 2024, 5G NTN Presentation, M. Petry

## Slide 4
Other Proprietary Mobile Satellite Solutions
Snapdragon Satellite
Garmin inReach
Skylo / Quectel / MediaTek
Beidou
4
GRCon 18th Sept. 2024, 5G NTN Presentation, M. Petry

## Slide 5
Cellular Standard-based Solutions
Starlink Direct-to-Cell
AST SpaceMobile
5
GRCon 18th Sept. 2024, 5G NTN Presentation, M. Petry

## Slide 6
Non-Terrestrial Networks in the Cellular Standards
1
6
GRCon 18th Sept. 2024, 5G NTN Presentation, M. Petry

## Slide 7
Evolution of Mobile Networks
1 Global System for Mobile Communication 2 General Packet Radio Service 3 Enhanced Data Rate for Global Evolution 4 Universal Mobile Telecommunications System 5 High Speed Packet Access 6 Long Term Evolution 7 LTE Advanced 8 New Radio *Analog service only, no data
40 Kbps*
0.5 – 1 s
200 kHz
1 G
2 G
3 G
4 G
5 G
6 G
1 G
2 G
2.5 G
3.9 G
Rel. 8
1981
1990
1993
2001
2006
2010
2015
2018
2020
2024
2030
C-Net NMT AMPS TACS
GSM1
IS-95A
GPRS2
IS-95B
EDGE3
UMTS4
CDMA 2000
HSDPA5
HSPA+
1xEV-D0
LTE6 (CAT 4)
LTE-
Adv.6
(CAT 6)
LTE-
Adv. Pro
(CAT 11)
LTE / NR8
Non-SA / SA
4.5 G
Rel. 10
4.9 G
Rel. 13/14
3.5 G
Rel. 5-7
3 G
Rel. 99
5 G
Rel. 15 - 17
5.5 G
Rel. 18 - 20
6 G
Rel. 21?
2.4 Kbps*
> 1s
30 kHz
9.6 Kbps*
0.5 – 1 s
200 kHz
150 Mbps
50 ms
20 MHz
600/1200 Mbps
15 ms
640 MHz
300 Mbps
15-50 ms
100 MHz
7.2/42 Mbps
69-75 ms
5 MHz
384 Kbps
O(100 ms)
200 kHz
< 1.9 GHz
< 2.1 GHz
< 2.5 GHz
FR1: < 6 GHz - FR2: < 95 GHz
< 10 Gbps
> 1 ms
700 MkHz
7
GRCon 18th Sept. 2024, 5G NTN Presentation, M. Petry
Satellites come here

## Slide 8
5G NTN Use Cases
8
GRCon 18th Sept. 2024, 5G NTN Presentation, M. Petry

## Slide 9
Satellites provide a direct connectivity option to remote / hard-to-reach locations
Satellites provide a connectivity to wireless towers, access points and the cloud
Satellites provide a direct
and/or complementary
connection for users on the move
Satellites deliver content
complementing terrestrial
broadband (as well as direct
broadband connectivity in
some cases)
Satellite „Sweet Spots“ in the 5G Ecosystem
TRUNKING & HEAD-END FEED
BACKHAULING & TOWER FEED
COMMS
ON THE MOVE
HYBRID
MULTIPLAY
9
GRCon 18th Sept. 2024, 5G NTN Presentation, M. Petry

## Slide 10
5G NTN Performance Goals
Source: 3GPP TR22.261 (19.7.0) „Service requirements for the 5G system; Stage 1” Table 7.4.2-1. Example Calculations based on SC4 and SC9
[1] Mbit/s
[100] Kbit/s
Handheld
50 Mbit/s
25 Mbit/s
Vehicle
mounted
Downlink Link-Budget
Uplink Link-Budget
 | Frequency | TX: EIRP [dBm] | RX: G/T [dB/T] | BW [MHz] | Path Loss [dB] | Add. L. [dB] | CNR [dB] | Shannon-Limit Data-Rate
LEO | S-Band | 78.8 | -31.6 | 30 | 159.1 | 5.3 | 6.6 | 22.37 Mbit/s
GEO | S-Band | 103.8 | -31.6 | 30 | 190.6 | 5.3 | 0.0 | 9.03 Mbit/s
 | Frequency | TX: EIRP [dBm] | RX: G/T [dB/T] | BW [MHz] | Path Loss [dB] | Add. Losses [dB] | CNR [dB] | Shannon-Limit Data-Rate
LEO | S-Band | 23 | 1.1 | 0.4 | 159.1 | 5.2 | 2.8 | 185.2 Kbit/s
GEO | S-Band | 23 | 19 | 0.4 | 190.6 | 5.4 | -10.9 | 13.57 Kbit/s
Assumptions: Full Target Resource Utilization, No Interference, No Frequency Re-Use, Ideal Channel Conditions
10
GRCon 18th Sept. 2024, 5G NTN Presentation, M. Petry

## Slide 11
5G Satellite Integration Architecture
2
11
GRCon 18th Sept. 2024, 5G NTN Presentation, M. Petry

## Slide 12
5G – The Land of Abbreviations
12
GRCon 18th Sept. 2024, 5G NTN Presentation, M. Petry

## Slide 13
5G Base Station Architecture Primer
NG
User-Equipment
Base station (gNB)
5G Core Network
N6
Data Network
NR-Uu
Downlink
RF
PHY
MAC
Radio Link Control
Packet Data Convergence
Protocol
Service Data Adaption Protocol
RF
PHY
MAC
Radio Link Control
Packet Data Convergence
Protocol
Service Data Adaption Protocol
Uplink
5G Stack Layers
Central Unit
Distributed Unit
Idea: Functional Split into Central Unit (CU) and Distributed Unit (DU)
Split Boundary
13
GRCon 18th Sept. 2024, 5G NTN Presentation, M. Petry
Notes: Why Split the Base station in two parts?
Serve multiple locations with 1 gNB
2
3

## Slide 14
PHY
PHY
Inter-PHY / eCPRI splits
10 – 30 Gbps
5G gNodeB Functional Split Options
RF
MAC
RLC
PDCP
SDAP
Downlink
Coding
Rate Matching
Scrambling
Modulation
Layer Mapping
Resource Element Mapping
Beamforming
IFFT
CP Insertion
RF
MAC
RLC
PDCP
SDAP
Uplink
Decoding
Rate Matching
Descrambling
Demodulation
IDFT
Equalizer
Diversity Combiner
Channel Estimation
Resource Element Demapping
Port Reduction
FFT
CP removal
F1-Interface
4 Gbps
CPRI
160 Gbps
Option 7.2
Option 7.1
Option 7.3
14
GRCon 18th Sept. 2024, 5G NTN Presentation, M. Petry

## Slide 15
5G NTN Architecture - Categories
Transparent Satellite
Regenerative Satellite
gNodeB
in space
gNodeB
On ground
Gateway
Gateway
5G Core Network
5G-NR Waveform
5G-NR Waveform
5G Backhaul
Transparent Architecture
Regenerative Architecture
5G-NR Waveform
NR Uu
NR Uu
NR Uu
NG
NG
NG
15
GRCon 18th Sept. 2024, 5G NTN Presentation, M. Petry

## Slide 16
Regenerative vs. Transparent - V2V Case Study
V2V-Link
Phase 1
Intra gNodeB communication
Round-Trip + 5G Processing Time
Regenerative [Transparent]:
LEO: 61.5 [113] ms
GEO: 1090 [2175,8] ms
Factor 0.5
Source for RT + Processing times: 3GPP TR38.821 (V16.2.0) „Solutions for NR to support non-terrestrial networks (NTN)” Table 7.1-1. 2x 5 ms Processing time assumed. Roundtrip is defined between vehicles. Worst-case propagtation delay assumed.
Winner: Regenerative
16
GRCon 18th Sept. 2024, 5G NTN Presentation, M. Petry

## Slide 17
Regenerative vs. Transparent – Inter gNB Handover
V2V-Link
Phase 1
Phase 2a
Inter-Satellite Link
Xn
Intra gNodeB communication
Handover + Inter gNodeB communication
1 https://openairinterface.org/wp-content/uploads/2022/11/4-GTRI.pdf Geoergia Tech Research Institute
Inter gNodeB handover
5GC-assisted (N2-based)
handover procedure time:
Regenerative [Transparent]
LEO: 163,9 [112] ms
GEO: 2742,3 [1659,38] ms
Factor 1.5
ISL-assisted (Xn-based) handover procedure time:
LEO: 104,4 ms
GEO: 1663,65 ms
Factor 1
5G Handover Protocol 1
5GC
5G Handover Protocol with Inter-gNB Link
5GC
Target gNB
Source gNB
UE
No Winner
17
GRCon 18th Sept. 2024, 5G NTN Presentation, M. Petry
Notes: LEO Transparent:
ue - gnb1: 2: 2x 25.77
ue - gnb2: 1: 1x 25.77
gnb1-core: 4: 4x 5? ms
gnb2-core: 3: 3x 5? ms
Total: 112
LEO Regen:
ue - gnb1: 2: 2x 12.89
ue - gnb2: 1: 1x 12.89
gnb1-core: 4: 4x 12.89 + 5?
gnb2-core: 3: 3x 12.89 + 5?
Total: 163,9 (Factor 1,4633928571428571428571428571429 worse)
GEO Transparent:
ue - gnb1: 2: 2x 541.46 ms
ue - gnb2: 1: 1x 541.46 ms
gnb1-core: 4: 4x 5? ms
gnb2-core: 3: 3x 5? ms
Total: 1659,38 ms
GEO Regen:
ue - gnb1: 2: 2x 270.73 ms
ue - gnb2: 1: 1x 270.73 ms
gnb1-core: 4: 4x 270.73 + 5? ms
gnb2-core: 3: 3x 270.73 + 5? ms
Total: 2742,3 ms (Factor 1,6526051898901999541997613566513 worse)
LEO Regen (with ISL):
ue - gnb1: 2x 12.89
ue - gnb2: 1x 12.89
gnb1-gnb2: 3x 10ms
gnb1-core: 0
gnb2-core: 2x 12.89 +5
Total: 104,45 ms
GEO Regen (with ISL):
ue - gnb1: 2x 270.73 ms
ue - gnb2: 1x 270.73 ms
gnb1-gnb2: 3x 100ms
gnb1-core: 0
gnb2-core: 2x 270.73 ms +5
Total: 1663,65 ms
More info:
https://www.tetcos.com/pdf/Performance-analysis-of-5G-Handovers-using-NetSim.pdf

## Slide 18
Regenerative vs. Transparent – Intra gNB Handover
Phase 1
Phase 2b
Intra gNodeB communication
Intra gNodeB handover
Terrestrial
Non-Terrestrial
Handover between sectors within a base station
Sector radius: 20 km (2m aperture / G=30 dBi)
Satellite Ground Speed: 7.4 km/s
Sector-Change every 2.7 seconds for non-stationary sectors
20km
18
GRCon 18th Sept. 2024, 5G NTN Presentation, M. Petry

## Slide 19
Regenerative vs. Transparent – Inter-gNB Coms.
V2V-Link
Phase 1
Phase 2
Inter-Satellite Link
Xn
Phase 3
Intra gNodeB communication
Handover + Inter gNodeB communication
Intra gNodeB communication
Round-Trip + 5G Processing Time
Regenerative (Xn) [Transparent]:
LEO: 71,5 [123] ms
GEO: 1282 [2185,8] ms
Factor 0.58
Winner: Regenerative
19
GRCon 18th Sept. 2024, 5G NTN Presentation, M. Petry

## Slide 20
5G gNodeB Implementation on-board the Satellite
3
20
GRCon 18th Sept. 2024, 5G NTN Presentation, M. Petry

## Slide 21
OpenAirInterface
… is a 5G framework
Open-source
Developed by our partners
Big Community
5G gNodeB on AMD-Xilinx VERSAL
Adaptive System on Chip
… is a hybrid architecture integrating
Programmable Processors (CPU)
Programmable FPGA Fabric
Programmable Accelerator Engines
CPU
DUAL-CORE ARM® CORTEX™-A72
Application Processor
DUAL-CORE ARM CORTEX-R5F
Real-Time Processor
=> General Purpose Functions
FPGA
Look-up tables: 900k
Logic cells: ~2M
=> DSP Functions
Intelligent Engines
400 AI Engines
DSP Engines
=> AI Functions
AMD-Xilinx VERSAL™ aSoC
5G Software Stack
21
GRCon 18th Sept. 2024, 5G NTN Presentation, M. Petry

## Slide 22
Approach 1: OAI on VERSAL without HW acceleration
CPU
=> General Purpose Functions
FPGA
=> DSP Functions
CPU Resource Utilization Profiling by Function
Not used
22
GRCon 18th Sept. 2024, 5G NTN Presentation, M. Petry

## Slide 23
Approach 2: OAI on VERSAL with PHY HW acceleration
Preliminary Performance Evaluation: Inter-PHY Split Option 7.1
No Hardware Acceleration
no
no
no
yes
yes
yes
73 %
53 %
75 %
55 %
93 %
91 %
DFT/IDFT Hardware Acceleration
Resource utilization for multiple PHY configurations for HW-accelerated and non-HW-accelerated mode:
Evaluated PHY configurations:
CPU in saturation
20 % CPU Utilization Reduction with HW-accelerated DFT/IDFT
24
GRCon 18th Sept. 2024, 5G NTN Presentation, M. Petry

## Slide 24
Control Unit
RF Frontend
Re-Gen Module
Multi-Core
Processor
FPGA
VERSAL
Theia Processor
Harness
CAN / Space-Wire Bus
Slices
Fibre interconnect
Functional Slices
Re-Gen Module
Fibre connector
CAN / SpW
SX4000
(ASIC)
Fibre connector
SX4000
(ASIC)
FPGA Slice
NVRAM
Versal adaptive SoC
Supervisor
NVRAM
DDR4
DDR4
Optical transceiver
Fibre connector
CAN / SpW
1st stage conversion
Fibre
CAN
Control Unit
Slow i/o
Main MCU
Multi-Core Processor
Multi-Core Processor System
DDR4
DDR4
PCIe
Developed at
RF Frontend
A/D Converters
Up/Down Conversion
Optical Transceivers
AD9082
5G gNodeB
The Big Picture: gNodeB on Next-Gen Telecom-Sat. Processor
25
GRCon 18th Sept. 2024, 5G NTN Presentation, M. Petry
Notes: Eine kleine Intro zu den Komponenten (high-level) die ein neuer, ML-tauglicher Telekom-Satellit-Prozessor hat. Auch intro zu den typischen RF use-cases: Transparent (d.h., signal quasi nur empfangen, und verstärkt in eine andere Richtung abstrahlen), Re-Gen (Regeneration) (d.h., Signal wirklich demodulieren und decodieren und frisch neu generieren, damit gewinnt man ein paar dB, dafür ist es aufwendiger), und neu RF mit ML capabilities (z.B. für 5G/6G, allgemein gehalten)
Kleine Infos zu den verschiedenen Slices: Control (selbsterklärend), RF-Frontend (1.5 GHz bandbreite 4 ADC+4DAC, bis 28 GHz), Re-Gen (mit proprietary ASIC DVB-S2 standard), US-FPGA (Versal) ist speziell für AI optimiert (siehe später).

## Slide 25
AI Accelerator
• Efficient integration of
AI/ML into 5G stack
possible
• On-Chip Machine
Learning Inference
RF Frontend
• Mixed signal front-end
• 4x 16-Bit 12 GSPS DAC
• 2x 6 GSPS ADC
• On-Chip DSP processing
capabilities available
5G gNodeB
AMD-Xilinx VERSAL AI Core System-on-Chip
Network-on-Chip
Processing System*
Programmable Logic
Intelligent/AI Engines
Heterogeneous gNodeB Implementation Concept
Data Scheduling & Control of PL
*Application Processor ARM Cortex-A72
CNN, Dense
AI / ML
FFT / IFFT
Native DSP Support
FIR Filter / Conv.
not currently used
DDR4
Multi-Core Central Processing Unit
PCIe
Interpolation
RF Signal Handling
Upconversion
PHY-Transceivers
AD9082
Physical Layer Low & High
Lower 5G Stack
JESD 204C
Communication IP
HW accelerated
5G Layer
Non-5G Layer
powered by
• Design Partitioning on
VERSAL and external CPU
using internal
PHY-MAC Split
• Distributed Unit and
Central Unit on board
• Physical Layer accelerated
using Programmable Logic
RRC Layer
Upper 5G Stack
PDCP Layer
RLC Layer
MAC Layer
• Upper Layers Running on
Multi-Core CPU
Split
PHY
MAC
26
GRCon 18th Sept. 2024, 5G NTN Presentation, M. Petry

## Slide 26
Configurable sampling rate schemes
  Four 16-bit DACs: 3 GSPS to 12 GSPS
  Two 12-bit ADCs: 1.5 GSPS to 6 GSPS
  RF synthesis and sampling up to 7.5 GHz (3 dB RF bandwidth)
Maximum receive bandwidth of 3 GHz (Nyquist)
Maximum transmit bandwidth is configuration dependent
  Four transmit channels: 16-bit = 1.2 GHz IBW, 12-bit = 1.6 GHz IBW
  Two transmit channels: 16-bit = 2.4 GHz IBW, 12-bit = 3.2 GHz IBW
  One transmit channel: 4.8 GHz IBW for N' = 8-bit
Signal processing blocks supporting multiband
  Transmit: eight DUC paths shared by four DACs; up to 64× interpolation
  Receive: eight DDC paths shared by two ADCs; up to 96× decimation
Additional DSP features
  PA protection for transmit
  96-tap programmable filter per ADC; or 192 taps total for receive
  Timing adjustments for receive QEC optimization
Flexible on-chip PLL for clocking; multichip synchronization
Features & Specifications
AD9082
AD9082 mixed signal front-end (MxFE®)
26
GRCon 18th Sept. 2024, 5G NTN Presentation, M. Petry
Notes: This slide shows proof of this product’s strengths.

## Slide 27
Check out our 5G NTN Live Demo in the Exhibition
28
GRCon 18th Sept. 2024, 5G NTN Presentation, M. Petry

## Slide 28
The Future of Space Communications is Bright
29
GRCon 18th Sept. 2024, 5G NTN Presentation, M. Petry
5G NTN is going to come
It will revolutionize satellite access
… for the better of everyone
Excited?