## Slide 1
Real-Time FMCW Radar System for Waveform Optimization using SDRs
Shammi Doly
Ph.D. Candidate in Electrical Engineering
A work of Prof. Dr. Daniel W. Bliss
WISCA FutureG/CoE JRCs Research

## Slide 2
sdoly.grconf-24
Outline
Background
System Overview
Approaches and Challenges
Results and Analysis
HWIL Over-The-Air Demo

## Slide 3
sdoly.grconf-24
System Overview
Key Contribution
Develop a highly flexible real-time FMCW radar system for designing and testing different radar waveforms (e.g., triangular, sawtooth),
Waveform adaptive co-design technique in a single a real-time feedback loop for multi-user networks applications leveraging low-cost SDRs,
Explore the benefits radar waveform optimization, particularly through increasing RMS bandwidth, significantly boosting target detection performance by enhancing range resolution.

## Slide 4
sdoly.grconf-24
System Design
Contributions
VCO-based Chirp Design/ Waveform Selection
Spectrum Shaping/ Waveform Optimization
Delay Detection Test

## Slide 5
sdoly.grconf-24
Pulsed vs CW Radar
Most radars use pulsed waveforms
  The pulse is repeated each PRI
  Switch between transmit and receive modes (T/R modules)
  Duty cycles range from .1 to 10%
  Longer pulse means more integration (good)
PRI
Slow time
Target
Radar
CW Radar transmits and receives simultaneously
Self interference can potentially be huge
  Can literally blow up front ends
  Typically limited to lower power systems
Historically, often assumed to be pure tone waveform
  No ranging, just detection and Doppler estimation
Frequency-modulated continuous wave (FMCW)
  Provides both range and velocity information
  Complex
Courtesy: Dan’s lecture

## Slide 6
sdoly.grconf-24
Linear FM Waveforms
Radar Waveforms
(Chirp)
Chirp Spectral Cartoon
Power Spectral
Density (linear)
B = 4
T = 20
(t) sweeps linearly across a total bandwidth of B (hz) during the pulse duration 𝝉 (sec).
If B𝜏 >> 1 then, qualify as pulse compression waveform.
Courtesy: Dan’s lecture

## Slide 7
Spectral coverage becomes more uniform as pulse duration increases
sdoly.grconf-24
Range
  Cell ~ 1/Bandwidth
Angle
  Cell ~ 1/Aperture
Doppler
  Cell ~ 1/Duration
Pulse compression decouple energy and resolution
If B𝜏 >> 1 then, qualify as pulse compression waveform. ( Rayleigh bandwidth B = 1/ 𝜏)
Power Spectral
Density (linear)
B = 4
T = 20
Power Spectral
Density (linear)
B = 4
T = 100
Power Spectral
Density (linear)
dc.wikia.com
I Am Batman
B = 4
T = 1000
Courtesy: Dan’s lecture
FM Pulse Compression Chirp
Waveform Design
Only one free parameter in design of pulse radar -

## Slide 8
sdoly.grconf-24
System Design
Contributions
Radar Design/ Waveform Selection
Spectrum Shaping/ Waveform Optimization
Delay Detection Test

## Slide 9
sdoly.grconf-24
RF Convergence
(Background)
1S. Doly, A. R. Chiriyath, H. Mittelmann, D. Bliss, and S. Ragi, “Waveform codesign for radar-communications spectral coexistence via dynamic programming,” IEEE Transactions on Aerospace and Electronic Systems, 2022
Waveform Co-design Approach
We pose waveform design problem as--
partially observable Markov decision process (POMDP)1.
Dynamic programming approaches.
  Nominal belief-state optimization (NBO),
  Random sampling-multipath hypothesis propagation (RS-MHP)
Heterogeneous and large network we can consider Dec-POMDP.
Radar-comms system
Dynamic environment
Radar-comms receiver
POMDP planner
Learn
& decide
Measurement
of the system
Radar return+ comms sig
Transmitted
waveform
Waveform
selected
Relationship between an agent and its environment
FCC Allocation Chart
Courtesy: Dan’s lecture
Multi-access scenario
Goal : Optimization of Linear Frequency Modulation (LFM) chirp waveforms for optimal jt. performance.
Motivations / Benefits
  Spectrum Sharing
  Resource Efficiency
  Reduced Costs
  Next-Gen Wireless

## Slide 10
sdoly.grconf-24
Range (Delay) Estimation Uncertainty
( Importance of Spectrum Shaping)
Est. Perf. vs. CRLB Threshold Tradeoff
Pic Courtesy : Alex
Accurate delay estimation is crucial for determining the range of a target.
Cramér-Rao Bound (CRB) provides theoretical limit on the accuracy with which the delay of a signal can be estimated.
Target
Radar
Cramer-Rao Bound
(dB)
Courtesy: Dan’s lecture
More Bandwidth Higher the SNR
  improves the Fisher Information,
  leading to a lower CRB,
  more information about the delay.

## Slide 11
sdoly.grconf-24
System Design
Radar Design/ Waveform Selection
Spectrum Shaping
Radar Test -- > Stretch Processing

## Slide 12: Pulse Compression Stretch Processing – Cheap Chirp Trick
sdoly.grconf-24
Approximate matched filter
  Multiply by conjugate chirp at receiver
Exploit delay-Doppler degeneracy
  Delay produces frequency shift
  Estimate range with FFT
Delay translates into
beat frequency
Chirp Spectral Cartoon
Courtesy: Dan’s lecture
Reference Chirp and Return
Reference Chirp and Return
Overlapped section

## Slide 13
sdoly.grconf-24
GNU Radio Experimental Flowgraph
VCO-based chirp synthesizer
  Sawtooth
  Triangular
Chirp optimization
  Mask generator
  Feedback / message generator block
Stretch Processing
Chirp Synthesizer
Stretch Processing
Stretch Processing
Chirp Optimization
System Design
Transmitter
Receiver

## Slide 14
sdoly.grconf-24
VCO - based Chirp Synthesizers
GNU Radio Chirp Generation Flowgraph
GNU Radio Voltage-Controlled Oscillator - (VCO)
  input: float stream of control voltages
  output: float oscillator output
  VCO Sensitivity = (2 * 𝜋* BW / input volt)
  lag between the VCO I/Q samples output
  and a signal generator
Parameters
  Sample Rates(Hz)
  Sensitivity (radians/sec/(input unit)
  Amplitude
Triangular Chirp
  Up-sweep (0 – T/2)
  Down-sweep (T/2 – T)
Block Processing Latency
Sawtooth Chirp
Up-sweep only (0 to T)
Block Processing Latency

## Slide 15
sdoly.grconf-24
Spectrum Masking Flowgraph
Est. Perf. vs. CRLB Threshold Tradeoff
Pic Courtesy : Alex
Radar Optimal
Comms Optimal
Unweighted
Chirp Optimization : Spectral Masking Method
Feedback loop
Radar Optimal: Brms
Comms Optimal : Brms

## Slide 16
sdoly.grconf-24
Stretch Processing Flowgraph
Stretch Processing : Matched Filter Frequency Response
(Cheap trick)
  Matched Filter Peak
  Trade-off –
  Wider peak help improve signal-to-noise ratio (SNR) by increasing the total energy
  Narrower matched filter peak is crucial for achieving high resolution
Standard Chirp ~ (- 20dB)
Optimized Chirp ~ (11.56 dB)

## Slide 17
sdoly.grconf-24
More Bandwidth Higher the SNR
  improves the Fisher Information,
  leading to a lower CRB,
  more information about the delay.
RMS Bandwidth and Peak Detection
Cramér-Rao Bound (CRB)
SNR reduced due to increased distance
Filter failed to detect the peak
Optimize bandwidth (rms) ensure effective detection of the matched filter peak
fixed delay
Detected peak
Standard chirp
Optimized chirp
Unable to detect the peak
Peak detected
Standard chirp
Optimized chirp
Reference Chirp and Return
Reference Chirp and Return
Increased the delays

## Slide 18
sdoly.grconf-24
Conclusion and Future Research
Key Contribution
Develop a highly flexible real-time FMCW radar system for designing and testing different radar waveforms (e.g., triangular, sawtooth),
Waveform adaptive co-design technique in a single a real-time feedback loop for multi-user networks applications leveraging low-cost SDRs,
Explore the benefits radar waveform optimization, particularly through increasing RMS bandwidth, significantly boosting target detection performance by enhancing range resolution.
Challenges
GNU radio block processing latency
Indeterministic feedback loop
Est. Perf. vs. CRLB Threshold Tradeoff
Pic Courtesy : Alex
Next Step
Implement ISACs system
Real target detection
NLFM Waveform

## Slide 19
Thank You