## Slide 1: Enabling Integrated Circuit-Based Full-Duplex Wireless in GNU Radio
Alon S. Levin, Manav Kohli, Sasank Garikapati, Mahmood Baraani Dastjerdi, Harish Krishnaswamy, Gil Zussman, Igor Kadota, Tingjun Chen, Aravind Nagulu, Jin Zhou, Ivan Seskar

## Slide 2: Full-Duplex Communication
Simultaneous transmission and reception on the same frequency
  Increased system throughput and reduced latency
  More flexible use of wireless spectrum resources
  Suffers from self-interference (SI) due to transmitter leakage, requiring 70–110 dB of SI cancellation (SIC) across antenna, analog, and digital domains for successful operation
D. Bharadia, E. McMilin, and S. Katti. 2013. Full Duplex Radios. In Proc. ACM SIGCOMM’13.
A. Sabharwal, P. Schniter, D. Guo, D. W. Bliss, S. Rangarajan, and R. Wichman. 2014. In-Band Full-Duplex Wireless: Challenges and Opportunities. IEEE Journal on Selected Areas in Communications 32, 9 (2014), 1637–1652.

## Slide 3: Typical FD Transceiver

## Slide 4: RF Canceller Classes
Aravind Nagulu, Negar Reiskarimian, Tingjun Chen, Sasank Garikapati, Igor Kadota, Tolga Dinc, Sastry Lakshmi Garimella, Manav Kohli, Alon Simon Levin, Gil Zussman, and Harish Krishnaswamy. Doubling Down on Wireless Capacity: A Review of Integrated Circuits, Systems, and Networks for Full Duplex. Proceedings of the IEEE, 112(5):405–432, 2024.
Phase- and Amplitude- Based Equalization
Frequency-Domain Equalization
Time-Domain Equalization
Notes: GEN-1 AND GEN-2 ARE MISPLACED – THESE ARE THE WRONG IMAGES

## Slide 5: Small Form-Factor Implementations
Phase- and Amplitude- Based Equalization
Time-Domain Equalization
Jin Zhou, Peter R. Kinget, and Harish Krishnaswamy, "A Blocker-Resilient Wideband Receiver with Low-Noise Active Two-Point Cancellation of >0dBm TX Leakage and TX Noise in RX Band for FDD/Co-Existence," in Proc. IEEE ISSCC'14, 2014.
Jin Zhou, Tsung-Hao Chuang, Tolga Dinc, and Harish Krishnaswamy, “Reconfigurable Receiver with >20MHz Bandwidth Self-Interference Cancellation Suitable for FDD, Co-existence and Full-Duplex Applications,” in Proc. IEEE ISSCC’15, 2015.
Aravind Nagulu, Sasank Garikapati, Igor Kadota, Mostafa Essawy, Tingjun Chen, Arun Natarajan, Gil Zussman, and Harish Krishnaswamy, “Full-duplex receiver with wideband multi-domain FIR cancellation based on stacked-capacitor, N-path switched-capacitor delay lines achieving >+54dB SIC Across 80MHz BW and >+15dBm TX power handling,” in Proc. IEEE ISSCC’21, 2021.
Frequency-Domain Equalization
Notes: GEN-1 AND GEN-2 ARE MISPLACED – THESE ARE THE WRONG IMAGES

## Slide 6: Gen-1 FD Radio: P&A Canceller
Circulator-based antenna interface
PCB emulates P&A canceller:
Configurable through GNU Radio
43dB of RF SIC across 5MHz
Harish Krishnaswamy, Gil Zussman, Jin Zhou, Jelena Marašević, Negar Reiskarimian, Tolga Dinc, and Tingjun Chen, "Full-Duplex in a Hand-Held Device - From Fundamental Physics to Complex Integrated Circuits, Systems and Networks: An Overview of the Columbia FlexICoN Project," in Proc. Asilomar Conference on Signals, Systems, and Computers (invited paper), Nov. 2016.

## Slide 7: Gen-2 FD Radio: FDE Canceller
Circulator-based antenna interface
PCB emulates FDE canceller:
Configurable through GNU Radio
50dB of RF SIC across 20MHz
Tingjun Chen, Mahmood Baraani Dastjerdi, Jin Zhou, Harish Krishnaswamy, and Gil Zussman, “Wideband Full-Duplex Wireless via Frequency-Domain Equalization: Design and Experimentation,” in Proc. ACM MobiCom'19, Oct. 2019.

## Slide 8: Gen-3 FD Radio: TDE Canceller
Dual-antenna interface
IC-based TDE canceller:
Configurable through GNU Radio
50dB of RF SIC across 50MHz
Alon S. Levin, Igor Kadota, Sasank Garikapati, Bo Zhang, Aditya Jolly, Manav Kohli, Mingoo Seok, Harish Krishnaswamy, and Gil Zussman, "Demo: Experimentation with Wideband Real-Time Adaptive Full Duplex Radios,“ in Proc. ACM SIGCOMM'23, Sept. 2023.

## Slide 9
Canceller RFIC
Full-Duplex Radio

## Slide 10
Canceller RFIC
Full-Duplex Radio

## Slide 11: Transmission: Packet Encapsulation
Pilot Slots
Each radio is assigned a pilot slot to ensure “quiet” time to measure the SI channel. In this figure, the radio is assigned Pilot Slot 0.
Payload
P0
P1

## Slide 12: Reception: Synchronization
Intra-Node Synchronization
Goal: to align the radio’s received SI signal with the corresponding transmission
Payload
P0

## Slide 13: Reception: Synchronization
Intra-Node Synchronization
Goal: to align the radio’s received SI signal with the corresponding transmission
Payload
P0

## Slide 14: Reception: Synchronization
Inter-Node Synchronization
Goal: to align radios’ transmissions such that the payloads overlap and pilot slots do not interfere
Payload
P0

## Slide 15: Reception: Synchronization
Inter-Node Synchronization
Payload
P1
P0
Goal: to align radios’ transmissions such that the payloads overlap and pilot slots do not interfere

## Slide 16: SI Channel Estimation
Transmit pilot symbols
Receive pilot symbols
Recover the SI channel:
Tx and Rx signal processing chains must be on the same master clock cycle!

## Slide 17: Digital SIC
Truncated Volterra series model:
Simplified first-order model:
Payload
P1
Payload
P1
Payload
P1
P0

## Slide 18: System Control and Coordination
Error Detection and Synchronization Control
Channel Estimation Control
Visualization
SPI Interface
Microcontroller
FPGA

## Slide 19
Tx Signal
SI after Ant. Int. + RFIC
SI after Ant. Int. + RFIC + DSIC
RFIC Optimization

## Slide 20: Evolution of SI Cancellation
Alon S. Levin, Igor Kadota, Sasank Garikapati, Bo Zhang, Aditya Jolly, Manav Kohli, Mingoo Seok, Harish Krishnaswamy, and Gil Zussman, "Demo: Experimentation with Wideband Real-Time Adaptive Full Duplex Radios,“ in Proc. ACM SIGCOMM'23, Sept. 2023.

## Slide 21: Open-Access FD Wireless Testbeds
Gen-1 FD Radio in ORBIT
Mobile Gen-1 FD Radio
Manav Kohli, Tingjun Chen, Mahmood Baraani Dastjerdi, Jackson Welles, Ivan Seskar, Harish Krishnaswamy, and Gil Zussman, “Open-access full-duplex wireless in the ORBIT and COSMOS testbeds,” Computer Networks, no. 199, p. 108420, Nov. 2021.

## Slide 22: Open-Access FD Wireless Testbeds
Gen-2 FD Radio in COSMOS
Manav Kohli, Tingjun Chen, Mahmood Baraani Dastjerdi, Jackson Welles, Ivan Seskar, Harish Krishnaswamy, and Gil Zussman, “Open-access full-duplex wireless in the ORBIT and COSMOS testbeds,” Computer Networks, no. 199, p. 108420, Nov. 2021.

## Slide 23: Open-Access FD Wireless Testbeds
Gen-3 FD Radio in COSMOS
Coming Soon!
Powered by GNU Radio

## Slide 24: Thank You!
More information:
flexicon.ee.columbia.edu
alon.s.levin@columbia.edu