## Slide 1: gr-pocketsdr: Bringing PocketSDR Front-Ends to GNU Radio and GNSS-SDR Ecosystem
Minhaj Uddin Ahmad
Ph.D. Student | mahmad12@crimson.ua.edu
Connected and Automated Mobility Lab @ UA
GNU Radio Conference 2026

## Slide 2: Global Navigation Satellite System
https://eos-gnss.com/wp-content/uploads/2023/04/GNSS-Infographic-1-1024x576.png
GNSS satellite signals are open for anyone / any device to receiver, for free, anywhere on earth.
With an SDR receiver, you can receiver the signals and process it in your laptop, turning your laptop into a GNSS receiver. This allows researchers to develop and test new algorithms and signal processing techniques.
Since GNSS signals are open, without any protection mechanism (mostly), there are safety and security concerns too, requiring active research in this area.

## Slide 3: We need more research for GNSS resiliency
https://www.researchgate.net/publication/382288564_CLPDI-based_Fast_Secure_Code_Estimation_and_Replay_Attacks_on_GNSS_Signals
Spoofing concept
Connected and Automated Mobility Lab

## Slide 4: Broad hardware support makes research accessible
Commodity SDR Hardware
Interface
PocketSDR
RTL-SDR
HackRF
USRP
LimeSDR
bladeRF
PlutoSDR
Processing Software
GNU Radio
GNSS-SDR
RTKLIB & Custom

## Slide 5: PocketSDR
MAX 2771
Cypress FX3
https://github.com/tomojitakasu/PocketSDR
https://www.datagnss.com/products/pocketsdr-gnss-receiver

## Slide 6: General Purpose GNSS Processing
https://github.com/tomojitakasu/PocketSDR
General Purpose - https://gnss-sdr.org/

## Slide 7: Traditional workflow
Offline file post-processing
Workaround for real-time processing

## Slide 8: Building the bridge for live reception
Cypress FX3

## Slide 9: Lets compare the gr-pocketsdr vs. ZMQ workaround
 | Pocket_SDR_Signal_Source | ZMQ_Signal_Source
Total CPU | 178.9 % | 205.1 %
Latency, median | 320.6 ms | 334.8 ms
Latency, worst case | 374.9 ms | 679.7 ms
Lag spread (jitter) | 58 ms | 236 ms
Wire rate, 1 channel | 16 MB/s | 64 MB/s
Reports lost samples | yes | no
Medians differ by 14 ms — worst cases differ by 305 ms

## Slide 10: Application – Lets test the PocketSDR clock
Clock offset = TCXO phase error vs GPS time
37.6 min unbroken fix, 22 584 epochs at 10 Hz
Frequency offset: −0.265 ppm
Stability floor 2.8×10⁻⁹ at τ = 43 s
Above the receiver noise floor throughout

## Slide 11: Open-source!
Source code available at GitHub
Merged with GNSS-SDR upstream, development branch

## Slide 12: Conclusions and future work
14.6 % less CPU than ZMQ workaround, 305 ms better at worst case jitter
4× less data transmission compared to ZMQ workaround
Get reports of ring-buffer overruns
Multi-frequency (GPS L1, L2, L5, Galileo) testing is open for future work
It works! (few quirks to work out)

## Slide 13
Thank You
Questions?
Contact: Minhaj Uddin Ahmad | mahmad12@crimson.ua.edu
Supported by the National Center for Transportation Cybersecurity and Resiliency (TraCR), a U.S. DOT National University Transportation Center, and by NSF Award #2340456.
Notes: Happy to take questions.