## Slide 1: How To Share Clocks For Phase Coherency (That suits your Needs)
Jan Schirok
Chief Engineer

## Slide 2
Enter to Win a USRP B206mini-i!
Scan the QR code to enter for your chance to win.
No purchase necessary. One entry per person.
Winner will be selected at random and notified after the event.
NI Ettus USRP B206mini-i
Visit the NI booth in the exhibit area to learn more!

## Slide 3: Introduction to Phase Coherency
Super Short, Super Brief

## Slide 4: Multi-Antenna Systems – Care about Synchronization
Rx
Rx
Direction Finding –
Tx-Tx / Rx-Rx coherence
Applications involving multiple antennas require
Systematic phase relations between channels (“Phase Coherence”)
Ant. array
Beamformer
…
…
Beamforming –
Tx-Tx / Rx-Rx coherence
High End SDRs with LO Sharing
(like the USRP X420)
Many SDRs (like the USRP) are designed with these applications in mind
SDRs with Phase Repeatability using Reference Sharing (like the USRP B310)
Based on the needs, SDRs scale in:
Frequency range
Bandwidth
…
Method/Level of Synchronization
Modelling helps with
understanding requirements:
Phase errors
Time offsets
Stability
Repeatability

## Slide 5: Application Requirements
What Level of Coherency will you need?

## Slide 6: Phase Coherency Requirements… Mapping Phase, Time, Stability, Repeatability
I want to do RF Direction Finding.
What’s the right device for the job?
Coverage of new WIFI bands
Scaling from 2 to 8 antennas
Signals with medium bandwidth
Consistency over a longer time
And, I want to rerun the measurement after a reboot with the same phase weights
What do you care about?
Direction is based on RF Phase accuracy
Wider Bandwidths turn into Time accuracy
For long durations we specify stability
Restarts are captured in repeatability
Coherency
Connoisseur
Synchronization
Supplier
A couple degree – maybe up to 10 degree offsets is usually good enough for me
How accurate does the phase need to be?
You should consider a device with repeatable phase – e.g. something that scales well to 8 channels using a Multi-Device-Synchronization cable…

## Slide 7: Map Applications
Direction Finding (AoA)
+ Beam Forming
Spectral Monitoring
Multi-User MIMO (Cooperative)
ISAC Research
Direction Finding (TDoA)
Distributed MIMO
General Themes – Your Application needs may differ!
Time
Accuracy
Phase
Accuracy
Drifting
Stable
Repeatable
Stable
Repeatable
Drifting
Teaching RF
Simpler RF
It’s not the application alone…
The used algorithm matters as well!
Notes: “Starting points” – but your application needs may differ

## Slide 8: Synchronization Methods
And accuracies…

## Slide 9: A little experiment…
Just clap along…
We’ll try a song…

## Slide 10: What does clapping tell us for synchronization?
Clapping = Matches your beat to my beat
Synchronization of Software Defined Radios is similar
  Your internal reference is pulled by an external reference
  The reference can be slow / or fast
  Faster usually has more accuracy (and We Will Rock You is fun to clap along)
    From 1 PPS, 10 MHz, 125 MHz to Shared LO – things increase accuracies
Note - following a beat is “over the air synchronization” – with some similarities to GPS 

## Slide 11: What about Single Device / Within a device?
Device Internal Channels
Time: Repeatable
Phase: Stable, some repeatable
Last Seen: Multi Channel Devices
Most of this presentation is BETWEEN DEVICES
What about – WITHIN A DEVICE? …The easy choice…
Time alignment likely repeatable & stable
Phase Accuracy is Device Specific
  Usually highly stable phase between channels
    Separate synthesizers (on different daughterboards) may decrease stability
  Repeatability depends on the architecture
    A list of USRPS with repeatable phase within the device: Specified: B310, X420, X440 Shared internal LO: B210, E320, TwinRX, N32x Seen working: UBX/OBX …

## Slide 12: Synchronization: Internal Reference between devices (aka – no synchronization)
Internal reference – SDR running “on its own”
(almost) Any SDR has this
Related specification: Reference/Frequency Accuracy
  Usually in PPM / PPB (# of 1E-6 or 1E-9)
  Reference frequency turns into – an RF frequency offset +1 ppm (1E-6) reference accuracy turns into 1kHz offset at 1 GHz RF (360 degrees phase in 1 ms!)
Time and Phase are drifting between devices
  Both based on reference accuracy
  Drift can be described with: Allan Variance / Allan deviation or Phase noise
Internal Reference
Time: Drifting
Phase: Drifting
Last Seen: Any SDR
Properties between Multiple Devices

## Slide 13: Synchronization: GPS / GNSS
GPS based synchronization uses an antenna (accessory) hooked up to the SDR … or to a Clock distribution like CDA-2990G
  Antenna requires direct view of the sky
  Receives signals from GPS satellites over the air
GPS data contains position (coordinates) and time/date
Time information is turned into high Frequency accuracy
  1E-9 (1ppb) or better can be achieved
  Stabilization will take some time (5..10 minutes, sometimes more)
Time is repeatable over many SDRs across the globe
  Time accuracy depends on many factors (model, clocking, weather conditions, antenna …) – expect roughly 2-digit nanoseconds
This is a uni-directional over-the-air synchronization with 20000..26000km distance (77ms worth of propagation time)
  Don’t expect a repeatable phase
GPS-based Synchronization
Time: Repeatable
Phase: Low stability
Last Seen: Mid/high end
Properties between Multiple Devices

## Slide 14: GPS-Based Synchronization
Any number of SDRs with
GPS antenna
SDR
GPS Ant
TX0
RX0
TX1
RX1
RF
PLL
GPS chip
SDR
GPS Ant
TX0
RX0
TX1
RX1
RF
PLL
GPS chip
SDR
GPS Ant
TX0
RX0
TX1
RX1
RF
PLL
GPS chip
SDR
GPS Ant
TX0
RX0
TX1
RX1
RF
PLL
GPS chip
SDR
GPS Ant
TX0
RX0
TX1
RX1
RF
PLL
GPS chip

## Slide 15: Network Based Synchronization
Network Based Synchronization
Time: Repeatable
Phase: Low stability
Last Seen: USRP N3xx
Fewer SDRs out there directly supporting network-based synchronization – e.g. USRP N3xx
Clock distribution devices available to also create PPS/10 MHz  can be used by many standard SDRs
1588 High Accuracy profile / White Rabbit: Time accuracy of << 1ns (down to picoseconds)
  Requires specific Ethernet infrastructure (White Rabbit Switches)
  Accuracy and effort/system complexity scale together
Works over fiber with long distances
Phase coherency – not repeatable but provides stability
Properties between Multiple Devices

## Slide 16: External Reference (10M+PPS)
External Reference
(10 MHz + PPS)
Time: Repeatable
Phase: Some Repeatability
Last Seen: Most SDRs
Most SDRs and RF instruments support 10 MHz as reference clock
PPS in addition provides accurate timing
Distribution devices help to synchronize multiple devices – like Octoclock CDA-2990
Device-dependent accuracies – but timing repeatability can get to very low levels, e.g. < 10 ps
Phase repeatability heavily depends on RF clocking – but can get down to 10s of degrees at RF (high temperature dependencies, settling times)

## Slide 17: Shared 10 MHz and PPS sync
Distribution
(e.g. OctoClock CDA-2990)
SDR
Clock in
PPS in
TX0
RX0
TX1
RX1
Transceiver
SDR
Clock in
PPS in
TX0
RX0
TX1
RX1
SDR
Clock in
PPS in
TX0
RX0
TX1
RX1
SDR
Clock in
PPS in
TX0
RX0
TX1
RX1
SDR
Clock in
PPS in
TX0
RX0
TX1
RX1
SDR
Clock in
PPS in
TX0
RX0
TX1
RX1
SDR
Clock in
PPS in
TX0
RX0
TX1
RX1
SDR
Clock in
PPS in
TX0
RX0
TX1
RX1
Transceiver
Transceiver
Transceiver
Transceiver
Transceiver
Transceiver
Transceiver
10MHz
10MHz
10MHz
10MHz
10MHz
10MHz
10MHz
10MHz
PLL
PLL
PLL
PLL
PLL
PLL
PLL
PLL
# of devices based on distribution device (some allow being cascaded)

## Slide 18: Multi Device Sync Cable
Multi Device Sync Cable
Time: Repeatable
Phase: Good Repeatability
Last Seen: USRP B310, N210
A couple SDRs are providing multi-device synchronization via extra cabling
  B310 is the latest USRP with that method
B310 specifically
  Shares higher reference frequency (“High Frequency Reference”)
  Still closes timing for 1 PPS
  Achieves higher accuracies for Time + Phase Repeatability & Stability than 10 MHz
  Star distribution for high symmetry (1 device shares clocks to 3 more + itself)
High synchronization accuracy
  A couple degrees of phase repeatability
  A couple picoseconds time repeatability
Properties between Multiple Devices

## Slide 19: Multi-Device Sync
Specific method for B310
First device shares reference
Wraps back to itself as well
B310
Clock in
Clock out
PPS out
PPS in
B310
Clock in
Clock out
PPS out
PPS in
B310
Clock in
Clock out
PPS out
PPS in
B310
Clock in
Clock out
PPS out
PPS in
TX0
RX0
TX1
RX1
TX0
RX0
TX1
RX1
TX0
RX0
TX1
RX1
TX0
RX0
TX1
RX1
High frequency reference

## Slide 20: LO Sharing
LO Sharing
Time: - (not shared)
Phase: Best repeatability
Last Seen: USRP X420, USRP N32x,TwinRX
LO Sharing helps with very accurate phase repeatability / stability between devices
  E.g. much better than 1 degree RMS at 18 GHz
Make sure the cabling is suitable (phase can be very temperature dependent)
New LO Sharing accessory for X420 – SignalCraft SC2510
  Distributes LO beyond 2 channel configurations
  Allows Cascading for > 8 channels
LO Sharing doesn’t help with accurate time  Still relies on another method like 10MHz+PPS reference for that
Properties between Multiple Devices

## Slide 21: X420 LO Sharing options
Multi-Device (4x4 and higher) via SignalCraft SC2510 (cascadable for > 8x8)
Simple 2x2 coherent system
Recommended 2x2 coherent system
(symmetric using passive splitter)

## Slide 22: Example Spec – Phase Accuracy
https://www.ni.com/docs/en-US/bundle/usrp-b310-enclosed-specs/page/specs.html

## Slide 23: Accuracy of Synchronization Methods between devices
Internal Reference
LO Sharing (X420, N32x, TwinRX)
GPS
External Reference (1PPS+10M)
Multi Device Sync (B310)
Network Sync (N3xx)
Time
Accuracy
Phase
Accuracy
Drifting
Stable
Repeatable
Stable
Repeatable
Drifting

## Slide 24: Summary

## Slide 25: Summary of synchronization methods – between devices
 |  | Internal | GPS | Network Sync | 10M + PPS (Octoclock) | Multi-Device-Sync Cable | LO Sharing
# of Devices |  |  |  |  | 64+ | Up to 4 | 64+
Example Devices |  | All SDRs | Usually mid/high-end; accessory | USRP N3xx | Most SDRs (10M) | N210 (2 dev) B310 (4 dev) | A couple high-end devices TwinRX DB USRP N32x USRP X420
Time offset between devices (“group delay”) | Stability | Drifts | Some stability | Stable | Stable | Very stable | [combine with other method]
 | Repeatability | Initial SW reset | 10s of ns | < 1 ns (White Rabbit) or much more | Repeatable (10ps .. 1 ns)* | Repeatable (< 5ps) | 
Phase offset between devices | Stability | Drifts | Low stability | Some stability ~10 degree | Some stability ~ 10 degree** | Stable (1 degree) | Very stable (<< 1 degree)
 | Repeatability | None | None | None | Some devices ~10..100 degree** | Repeatable** (< 10 degree) | Very repeatable (<< 1 degree)
 |  | Internal | GPS | Network Sync | 10M + PPS (Octoclock) | Multi-Device-Sync Cable | LO Sharing
# of Devices |  |  |  |  | 64+ | Up to 4 | 64+
Example Devices |  | All SDRs | Usually mid/high-end; accessory | USRP N3xx | Most SDRs (10M) | N210 (2 dev) B310 (4 dev) | A couple high-end devices TwinRX DB USRP N32x USRP X420
Time offset between devices (“group delay”) | Stability | Drifts | Some stability | Stable | Stable | Very stable | [combine with other method]
 | Repeatability | Initial SW reset | 10s of ns | < 1 ns (White Rabbit) or much more | Repeatable (10ps .. 1 ns)* | Repeatable (< 5ps) | 
Phase offset between devices | Stability | Drifts | Low stability | Some stability ~10 degree | Some stability ~ 10 degree** | Stable (1 degree) | Very stable (<< 1 degree)
 | Repeatability | None | None | None | Some devices ~10..100 degree** | Repeatable** (< 10 degree) | Very repeatable (<< 1 degree)
* Device dependent
** Device and frequency dependent

## Slide 26: Q&A